## Slide 1
Wiring Schematic - Node Summary
Node ID | Location | Radio Address | 12V Boards | 5V Boards | Input Boards | Num Blocks
C1 | Helix - Lower | 1 | 1 | 2 | 2 | 8
C2 | North - Lower | 12 | 2 | 2 | 3 | 7
C3 | North - Lower | 2 | 1 | 2 | 2 | 7
C4 | West - Lower | 3 | 1 | 2 | 2 | 5
C5 | West - Lower | 13 | 1 | 2 | 2 | 8
C6 | Peninsula - Lower | 4 | 1 | 2 | 2 | 8
C7 | Helix | 11 | 1 | 2 | 0 | 4
C8 | Helix - Upper | 21 | 1 | 2 | 2 | 8
C9 | North - Upper | 22 | 1 | 2 | 2 | 8
C10 | North - Upper | 32 | 1 | 1 | 0 | 0
C11 | West - Upper | 23 | 1 | 2 | 1 | 8
C12 | West - Upper | 14 | 1 | 2 | 2 | 8
C13 | Peninsula - Upper | 24 | 1 | 2 | 2 | 8

## Slide 2
Turnout Summary
Turnout | Node | Button | Feedback | Signals
Switch 113 | C1 | C1-IN2-1 | N:C1-IN1-1, R:C1-IN1-2 | S1-1, S1-3, S1-2
Switch 114 | C1 | C1-IN2-2 | N:C1-IN1-3, R:C1-IN1-4 | S1-4, S1-5
Switch 115 | C1 | C1-IN2-3 | N:C1-IN1-5, R:C1-IN1-6 | S1-6
Switch 107 | C2 | C2-IN2-1 | N:C2-IN1-1, R:C2-IN1-2 | S2-6
Switch 108 | C2 | C2-IN2-2 | N:C2-IN1-3, R:C2-IN1-4 | S2-7
Switch 109 | C2 | C2-IN2-3 | N:C2-IN1-5, R:C2-IN1-6 | S2-8, S2-5
Switch 110 | C2 | C2-IN2-4 | N:C2-IN1-7, R:C2-IN1-8 | S2-9, S2-1
Switch 111 | C2 | C2-IN2-5 | N:C2-IN3-1, R:C2-IN3-2 | S1-2, S2-4, S2-1
Switch 112 | C2 | C2-IN2-6 | N:C2-IN3-3, R:C2-IN3-4 | S4-1, S2-3
Switch 103 | C4 | C4-IN2-1 | N:C4-IN1-1, R:C4-IN1-2 | S3-10, S3-7
Switch 104 | C4 | C4-IN2-2 | N:C4-IN1-3, R:C4-IN1-4 | S3-11
Switch 105 | C4 | C4-IN2-3 | N:C4-IN1-5, R:C4-IN1-6 | S3-12
Switch 106 | C4 | C4-IN2-4 | N:C4-IN1-7, R:C4-IN1-8 | S3-13
Switch 117 | C5 | C5-IN2-1 | N:C5-IN1-1, R:C5-IN1-2 | 
Switch 118 | C5 | C5-IN2-2 | N:C5-IN1-3, R:C5-IN1-4 | 
Switch 119 | C5 | C5-IN2-3 | N:C5-IN1-5, R:C5-IN1-6 | 
Switch 100 | C6 | C6-IN2-1 | N:C6-IN1-1, R:C6-IN1-2 | S3-14
Switch 101 | C6 | C6-IN2-2 | N:C6-IN1-3, R:C6-IN1-4 | S1-1, S3-3
Turnout | Node | Button | Feedback | Signals
Switch 102 | C6 | C6-IN2-3 | N:C6-IN1-5, R:C6-IN1-6 | S3-1, S3-6, S3-7
Switch 116 | C6 | C6-IN2-4 | N:C6-IN1-7, R:C6-IN1-8 | 
SW127 | C7 | C8-IN2-3 | N:C8-IN1-5, R:C8-IN1-6 | S4-3, S4-1
SW129 | C7 | C8-IN2-2 | N:C8-IN1-3, R:C8-IN1-4 | S4-2
SW138 | C7 | C8-IN2-4 | N:C8-IN1-7, R:C8-IN1-8 | S4-4, S4-5
NIX | C8 | C8-IN2-1 | N:C8-IN1-1, R:C8-IN1-2 | S4-6, S4-5, S4-4
DJE | C9 | C9-IN2-1 | N:C9-IN1-1, R:C9-IN1-2 | S5-1, S5-5, S5-6
DJW | C9 | C9-IN2-2 | N:C9-IN1-3, R:C9-IN1-4 | S5-2, S5-4
SW124 | C10 | C9-IN2-3 | N:C9-IN1-5, R:C9-IN1-6 | S5-3, S5-4, S5-7
CBX | C11 | C11-IN1-7 | N:C11-IN1-1, R:C11-IN1-2 | S6-1, S6-2
SW143 | C11 | C11-IN1-8 | N:C11-IN1-3, R:C11-IN1-4 | S6-4, S6-5
SW144 | C12 | C12-IN2-1 | N:C12-IN1-1, R:C12-IN1-2 | S6-1, S6-4
SW145 | C12 | C12-IN2-2 | N:C12-IN1-3, R:C12-IN1-4 | S6-10
SW146 | C12 | C12-IN2-3 | N:C12-IN1-5, R:C12-IN1-6 | S6-11, S6-12
SW147 | C12 | C12-IN2-4 | N:C12-IN1-7, R:C12-IN1-8 | 
SW148 | C13 | C13-IN2-1 | N:C13-IN1-1, R:C13-IN1-2 | S6-1, S6-5
SW149 | C13 | C13-IN2-2 | N:C13-IN1-3, R:C13-IN1-4 | S6-14
SW150 | C13 | C13-IN2-3 | N:C13-IN1-5, R:C13-IN1-6 | S6-15

## Slide 3
Node C1 - Helix - Lower
C1-OU1 | 
C1-OU1-1 | Switch 113 N
C1-OU1-2 | Switch 113 R
C1-OU1-3 | Switch 114 N
C1-OU1-4 | Switch 114 R
C1-OU1-5 | Switch 115 N
C1-OU1-6 | Switch 115 R
C1-OU1-7 | Reserved
C1-OU1-8 | Reserved
C1-OU2 | 
C1-OU2-1 | S1-1 G
C1-OU2-2 | S1-1 Y
C1-OU2-3 | S1-1 R
C1-OU2-4 | S1-2 G
C1-OU2-5 | S1-2 Y
C1-OU2-6 | S1-2 R
C1-OU2-7 | 
C1-OU2-8 | C1 RELAY 1
C1-OU3 | 
C1-OU3-1 | S1-3 G
C1-OU3-2 | S1-3 Y
C1-OU3-3 | S1-3 R
C1-OU3-4 | S1-4 G
C1-OU3-5 | S1-4 Y
C1-OU3-6 | S1-4 R
C1-OU3-7 | 
C1-OU3-8 | 
C1-IN1 | 
C1-IN1-1 | Switch 113 N FB
C1-IN1-2 | Switch 113 R FB
C1-IN1-3 | Switch 114 N FB
C1-IN1-4 | Switch 114 R FB
C1-IN1-5 | Switch 115 N FB
C1-IN1-6 | Switch 115 R FB
C1-IN1-7 | 
C1-IN1-8 | 
C1-IN2 | 
C1-IN2-1 | Switch 113 BTN
C1-IN2-2 | Switch 114 BTN
C1-IN2-3 | Switch 115 BTN
C1-IN2-4 | 
C1-IN2-5 | 
C1-IN2-6 | 
C1-IN2-7 | 
C1-IN2-8 | 
C1 Blocks | 
C1-B1-1 | McKees Rocks
C1-B1-2 | McKeesport
C1-B2-1 | Switch 114
C1-B2-2 | Switch 115
C1-B3-1 | Switch 113b
C1-B3-2 | Switch 113a
C1-B4-1 | East Lead
C1-B4-2 | West Main Ext

## Slide 4
Node C2 - North - Lower
C2-OU1 | 
C2-OU1-1 | Switch 107 N
C2-OU1-2 | Switch 107 R
C2-OU1-3 | Switch 108 N
C2-OU1-4 | Switch 108 R
C2-OU1-5 | Switch 109 N
C2-OU1-6 | Switch 109 R
C2-OU1-7 | Switch 110 N
C2-OU1-8 | Switch 110 R
C2-OU2 | 
C2-OU2-1 | S2-1 G
C2-OU2-2 | S2-1 Y
C2-OU2-3 | S2-1 R
C2-OU2-4 | S2-2 G
C2-OU2-5 | S2-2 Y
C2-OU2-6 | S2-2 R
C2-OU2-7 | S2-8 Y
C2-OU2-8 | C2 RELAY 1
C2-OU3 | 
C2-OU3-1 | S2-9 G
C2-OU3-2 | S2-9 R
C2-OU3-3 | S2-9 Y
C2-OU3-4 | S2-4 G
C2-OU3-5 | S2-4 Y
C2-OU3-6 | S2-4 R
C2-OU3-7 | S2-8 G
C2-OU3-8 | S2-8 R
C2-IN1 | 
C2-IN1-1 | Switch 107 N FB
C2-IN1-2 | Switch 107 R FB
C2-IN1-3 | Switch 108 N FB
C2-IN1-4 | Switch 108 R FB
C2-IN1-5 | Switch 109 N FB
C2-IN1-6 | Switch 109 R FB
C2-IN1-7 | Switch 110 N FB
C2-IN1-8 | Switch 110 R FB
C2-IN2 | 
C2-IN2-1 | Switch 107 BTN
C2-IN2-2 | Switch 108 BTN
C2-IN2-3 | Switch 109 BTN
C2-IN2-4 | Switch 110 BTN
C2-IN2-5 | Switch 111 BTN
C2-IN2-6 | Switch 112 BTN
C2-IN2-7 | 
C2-IN2-8 | 
C2-IN3 | 
C2-IN3-1 | Switch 111 N FB
C2-IN3-2 | Switch 111 R FB
C2-IN3-3 | Switch 112 N FB
C2-IN3-4 | Switch 112 R FB
C2-IN3-5 | 
C2-IN3-6 | 
C2-IN3-7 | 
C2-IN3-8 | 

## Slide 5
Node C3 - North - Lower (cont'd)
C3-OU1 | 
C3-OU1-1 | 
C3-OU1-2 | 
C3-OU1-3 | 
C3-OU1-4 | 
C3-OU1-5 | 
C3-OU1-6 | 
C3-OU1-7 | 
C3-OU1-8 | 
C3-OU2 | 
C3-OU2-1 | S2-5 G
C3-OU2-2 | S2-5 Y
C3-OU2-3 | S2-5 R
C3-OU2-4 | S2-3 G
C3-OU2-5 | S2-3 Y
C3-OU2-6 | S2-3 R
C3-OU2-7 | S2-6 Y
C3-OU2-8 | C3 RELAY 1
C3-OU3 | 
C3-OU3-1 | S2-6 G
C3-OU3-2 | S2-6 R
C3-OU3-3 | S2-7 G
C3-OU3-4 | S2-7 R
C3-OU3-5 | S2-7 Y
C3-OU3-6 | 
C3-OU3-7 | 
C3-OU3-8 | 
C3-IN1 | 
C3-IN1-1 | Switch 107 N FB
C3-IN1-2 | Switch 107 R FB
C3-IN1-3 | Switch 108 N FB
C3-IN1-4 | Switch 108 R FB
C3-IN1-5 | Switch 109 N FB
C3-IN1-6 | Switch 109 R FB
C3-IN1-7 | Switch 110 N FB
C3-IN1-8 | Switch 110 R FB
C3-IN2 | 
C3-IN2-1 | Switch 107 BTN
C3-IN2-2 | Switch 108 BTN
C3-IN2-3 | Switch 109 BTN
C3-IN2-4 | Switch 110 BTN
C3-IN2-5 | 
C3-IN2-6 | 
C3-IN2-7 | 
C3-IN2-8 | 
C3 Blocks | 
C3-B1-1 | Main West
C3-B1-2 | Unused
C3-B2-1 | Main East
C3-B2-2 | Yard Track 5
C3-B3-1 | Yard Track 4
C3-B3-2 | Yard Track 3
C3-B4-1 | Yard Track 2
C3-B4-2 | Yard Track 1

## Slide 6
Node C4 - West - Lower
C4-OU1 | 
C4-OU1-1 | Switch 103 N
C4-OU1-2 | Switch 103 R
C4-OU1-3 | Switch 104 N
C4-OU1-4 | Switch 104 R
C4-OU1-5 | Switch 105 N
C4-OU1-6 | Switch 105 R
C4-OU1-7 | Switch 106 N
C4-OU1-8 | Switch 106 R
C4-OU2 | 
C4-OU2-1 | S3-6 G
C4-OU2-2 | S3-6 Y
C4-OU2-3 | S3-6 R
C4-OU2-4 | S3-7 G
C4-OU2-5 | S3-7 Y
C4-OU2-6 | S3-7 R
C4-OU2-7 | S3-11 Y
C4-OU2-8 | C4 RELAY 1
C4-OU3 | 
C4-OU3-1 | S3-8 G
C4-OU3-2 | S3-8 Y
C4-OU3-3 | S3-8 R
C4-OU3-4 | S3-9 G
C4-OU3-5 | S3-9 Y
C4-OU3-6 | S3-9 R
C4-OU3-7 | S3-11 G
C4-OU3-8 | S3-11 R
C4-IN1 | 
C4-IN1-1 | Switch 103 N FB
C4-IN1-2 | Switch 103 R FB
C4-IN1-3 | Switch 104 N FB
C4-IN1-4 | Switch 104 R FB
C4-IN1-5 | Switch 105 N FB
C4-IN1-6 | Switch 105 R FB
C4-IN1-7 | Switch 106 N FB
C4-IN1-8 | Switch 106 R FB
C4-IN2 | 
C4-IN2-1 | Switch 103 BTN
C4-IN2-2 | Switch 104 BTN
C4-IN2-3 | Switch 105 BTN
C4-IN2-4 | Switch 106 BTN
C4-IN2-5 | 
C4-IN2-6 | 
C4-IN2-7 | 
C4-IN2-8 | 
C4 Blocks | 
C4-B1-1 | Switch 116
C4-B1-2 | Switch 103
C4-B2-1 | Switch 104
C4-B2-2 | Unused
C4-B3-1 | Switch 105
C4-B3-2 | Unused
C4-B4-1 | Switch 106
C4-B4-2 | Unused

## Slide 7
Node C5 - West - Lower (cont'd)
C5-OU1 | 
C5-OU1-1 | S3-10 G
C5-OU1-2 | S3-10 Y
C5-OU1-3 | S3-10 R
C5-OU1-4 | S3-12 G
C5-OU1-5 | S3-12 R
C5-OU1-6 | S3-12 Y
C5-OU1-7 | S3-14 G
C5-OU1-8 | S3-14 R
C5-OU2 | 
C5-OU2-1 | S3-4 G
C5-OU2-2 | S3-4 Y
C5-OU2-3 | S3-4 R
C5-OU2-4 | S3-5 G
C5-OU2-5 | S3-5 Y
C5-OU2-6 | S3-5 R
C5-OU2-7 | S3-14 Y
C5-OU2-8 | 
C5-OU3 | 
C5-OU3-1 | Switch 117 N
C5-OU3-2 | Switch 117 R
C5-OU3-3 | Switch 118 N
C5-OU3-4 | Switch 118 R
C5-OU3-5 | Switch 119 N
C5-OU3-6 | Switch 119 R
C5-OU3-7 | 
C5-OU3-8 | 
C5-IN1 | 
C5-IN1-1 | Switch 117 N FB
C5-IN1-2 | Switch 117 R FB
C5-IN1-3 | Switch 118 N FB
C5-IN1-4 | Switch 118 R FB
C5-IN1-5 | Switch 119 N FB
C5-IN1-6 | Switch 119 R FB
C5-IN1-7 | 
C5-IN1-8 | 
C5-IN2 | 
C5-IN2-1 | Switch 117 BTN
C5-IN2-2 | Switch 118 BTN
C5-IN2-3 | Switch 119 BTN
C5-IN2-4 | 
C5-IN2-5 | 
C5-IN2-6 | 
C5-IN2-7 | 
C5-IN2-8 | 
C5 Blocks | 
C5-B1-1 | Yard T6
C5-B1-2 | Switch 118
C5-B2-1 | Switch 117 (TO8)
C5-B2-2 | Switch 117 (TO6)
C5-B3-1 | Yard T11
C5-B3-2 | Yard T10
C5-B4-1 | Yard T9
C5-B4-2 | Switch 119

## Slide 8
Node C6 - Peninsula - Lower
C6-OU1 | 
C6-OU1-1 | Switch 100 N
C6-OU1-2 | Switch 100 R
C6-OU1-3 | Switch 101 N
C6-OU1-4 | Switch 101 R
C6-OU1-5 | Switch 102 N
C6-OU1-6 | Switch 102 R
C6-OU1-7 | Switch 116 N
C6-OU1-8 | Switch 116 R
C6-OU2 | 
C6-OU2-1 | S3-1 G
C6-OU2-2 | S3-1 Y
C6-OU2-3 | S3-1 R
C6-OU2-4 | S3-13 G
C6-OU2-5 | S3-13 R
C6-OU2-6 | S3-13 Y
C6-OU2-7 | 
C6-OU2-8 | C6 RELAY 1
C6-OU3 | 
C6-OU3-1 | S3-2 G
C6-OU3-2 | S3-2 Y
C6-OU3-3 | S3-2 R
C6-OU3-4 | S3-3 G
C6-OU3-5 | S3-3 Y
C6-OU3-6 | S3-3 R
C6-OU3-7 | 
C6-OU3-8 | 
C6-IN1 | 
C6-IN1-1 | Switch 100 N FB
C6-IN1-2 | Switch 100 R FB
C6-IN1-3 | Switch 101 N FB
C6-IN1-4 | Switch 101 R FB
C6-IN1-5 | Switch 102 N FB
C6-IN1-6 | Switch 102 R FB
C6-IN1-7 | Switch 116 N FB
C6-IN1-8 | Switch 116 R FB
C6-IN2 | 
C6-IN2-1 | Switch 100 BTN
C6-IN2-2 | Switch 101 BTN
C6-IN2-3 | Switch 102 BTN
C6-IN2-4 | Switch 116 BTN
C6-IN2-5 | 
C6-IN2-6 | 
C6-IN2-7 | 
C6-IN2-8 | 
C6 Blocks | 
C6-B1-1 | Switch 101
C6-B1-2 | Switch 100
C6-B2-1 | West Yard Track 2
C6-B2-2 | West Yard Track 1
C6-B3-1 | Switch 102
C6-B3-2 | Block 100-102
C6-B4-1 | East Main Ext
C6-B4-2 | Yard T1

## Slide 9
Node C7 - Helix
C7-OU1 | 
C7-OU1-1 | Switch 1129 N
C7-OU1-2 | Switch 1129 R
C7-OU1-3 | Switch 1127 N
C7-OU1-4 | Switch 1127 R
C7-OU1-5 | Switch 10038 N
C7-OU1-6 | Switch 10038 R
C7-OU1-7 | 
C7-OU1-8 | 
C7-OU2 | 
C7-OU2-1 | S1-5 G
C7-OU2-2 | S1-5 R
C7-OU2-3 | S1-5 Y
C7-OU2-4 | S1-6 G
C7-OU2-5 | S1-6 R
C7-OU2-6 | S1-6 Y
C7-OU2-7 | 
C7-OU2-8 | C11 RELAY 1
C7-OU3 | 
C7-OU3-1 | S4-6 G
C7-OU3-2 | S4-6 R
C7-OU3-3 | S4-6 Y
C7-OU3-4 | S4-7 G
C7-OU3-5 | S4-7 R
C7-OU3-6 | S4-7 Y
C7-OU3-7 | 
C7-OU3-8 | 
C7 Blocks | 
C7-B1-1 | Helix Inner A
C7-B1-2 | Helix Outer A
C7-B2-1 | Helix Inner B
C7-B2-2 | Helix Outer B

## Slide 10
Node C8 - Helix - Upper
C8-OU1 | 
C8-OU1-1 | NIX N
C8-OU1-2 | NIX R
C8-OU1-3 | Reserved
C8-OU1-4 | Reserved
C8-OU1-5 | Reserved
C8-OU1-6 | Reserved
C8-OU1-7 | Reserved
C8-OU1-8 | Reserved
C8-OU2 | 
C8-OU2-1 | S4-1 G
C8-OU2-2 | S4-1 Y
C8-OU2-3 | S4-1 R
C8-OU2-4 | S4-2 G
C8-OU2-5 | S4-2 Y
C8-OU2-6 | S4-2 R
C8-OU2-7 | S4-5 Y
C8-OU2-8 | C6 RELAY 1
C8-OU3 | 
C8-OU3-1 | S4-3 G
C8-OU3-2 | S4-3 Y
C8-OU3-3 | S4-3 R
C8-OU3-4 | S4-4 G
C8-OU3-5 | S4-4 Y
C8-OU3-6 | S4-4 R
C8-OU3-7 | S4-5 G
C8-OU3-8 | S4-5 R
C8-IN1 | 
C8-IN1-1 | NIX N FB
C8-IN1-2 | NIX R FB
C8-IN1-3 | Switch 1129 N FB
C8-IN1-4 | Switch 1129 R FB
C8-IN1-5 | Switch 1127 N FB
C8-IN1-6 | Switch 1127 R FB
C8-IN1-7 | Switch 10038 N FB
C8-IN1-8 | Switch 10038 R FB
C8-IN2 | 
C8-IN2-1 | NIX BTN
C8-IN2-2 | Switch 1129 BTN
C8-IN2-3 | Switch 1127 BTN
C8-IN2-4 | Switch 10038 BTN
C8-IN2-5 | 
C8-IN2-6 | 
C8-IN2-7 | 
C8-IN2-8 | 
C8 Blocks | 
C8-B1-1 | NIL A
C8-B1-2 | NIL B
C8-B2-1 | SW129
C8-B2-2 | Outer Leg
C8-B3-1 | SW127
C8-B3-2 | SW138
C8-B4-1 | SW139,140
C8-B4-2 | SW125,126

## Slide 11
Node C9 - North - Upper
C9-OU1 | 
C9-OU1-1 | DJE N
C9-OU1-2 | DJE R
C9-OU1-3 | DJW N
C9-OU1-4 | DJW R
C9-OU1-5 | Reserved
C9-OU1-6 | Reserved
C9-OU1-7 | Reserved
C9-OU1-8 | Reserved
C9-OU2 | 
C9-OU2-1 | S5-1 G
C9-OU2-2 | S5-1 Y
C9-OU2-3 | S5-1 R
C9-OU2-4 | S5-2 G
C9-OU2-5 | S5-2 Y
C9-OU2-6 | S5-2 R
C9-OU2-7 | S5-5 Y
C9-OU2-8 | C7 RELAY 1
C9-OU3 | 
C9-OU3-1 | S5-3 G
C9-OU3-2 | S5-3 Y
C9-OU3-3 | S5-3 R
C9-OU3-4 | S5-4 G
C9-OU3-5 | S5-4 Y
C9-OU3-6 | S5-4 R
C9-OU3-7 | S5-5 G
C9-OU3-8 | S5-5 R
C9-IN1 | 
C9-IN1-1 | DJE N FB
C9-IN1-2 | DJE R FB
C9-IN1-3 | DJW N FB
C9-IN1-4 | DJW R FB
C9-IN1-5 | Switch 1124 N FB
C9-IN1-6 | Switch 1124 R FB
C9-IN1-7 | 
C9-IN1-8 | 
C9-IN2 | 
C9-IN2-1 | DJE BTN
C9-IN2-2 | DJW BTN
C9-IN2-3 | Switch 1124 BTN
C9-IN2-4 | 
C9-IN2-5 | 
C9-IN2-6 | 
C9-IN2-7 | 
C9-IN2-8 | 
C9 Blocks | 
C9-B1-1 | Closet Inner
C9-B1-2 | Closet Outer
C9-B2-1 | SW124
C9-B2-2 | SW122,123
C9-B3-1 | SW120
C9-B3-2 | SW121
C9-B4-1 | Outside Outer A
C9-B4-2 | Outside Inner A

## Slide 12
Node C10 - North - Upper (cont'd)
C10-OU1 | 
C10-OU1-1 | Switch 1124 N
C10-OU1-2 | Switch 1124 R
C10-OU1-3 | 
C10-OU1-4 | 
C10-OU1-5 | 
C10-OU1-6 | 
C10-OU1-7 | 
C10-OU1-8 | 
C10-OU2 | 
C10-OU2-1 | S5-6 G
C10-OU2-2 | S5-6 Y
C10-OU2-3 | S5-6 R
C10-OU2-4 | S5-7 G
C10-OU2-5 | S5-7 R
C10-OU2-6 | S5-7 Y
C10-OU2-7 | 
C10-OU2-8 | 

## Slide 13
Node C11 - West - Upper
C11-OU1 | 
C11-OU1-1 | CBX N
C11-OU1-2 | CBX R
C11-OU1-3 | Switch 10043 N
C11-OU1-4 | Switch 10043 R
C11-OU1-5 | Reserved
C11-OU1-6 | Reserved
C11-OU1-7 | 
C11-OU1-8 | 
C11-OU2 | 
C11-OU2-1 | S6-6 G
C11-OU2-2 | S6-6 Y
C11-OU2-3 | S6-6 R
C11-OU2-4 | S6-8 G
C11-OU2-5 | S6-8 Y
C11-OU2-6 | S6-8 R
C11-OU2-7 | S6-12 Y
C11-OU2-8 | C10 RELAY 1
C11-OU3 | 
C11-OU3-1 | S6-15 G
C11-OU3-2 | S6-15 R
C11-OU3-3 | S6-15 Y
C11-OU3-4 | S6-14 G
C11-OU3-5 | S6-14 R
C11-OU3-6 | S6-14 Y
C11-OU3-7 | S6-12 G
C11-OU3-8 | S6-12 R
C11-IN1 | 
C11-IN1-1 | CBX N FB
C11-IN1-2 | CBX R FB
C11-IN1-3 | Switch 10043 N FB
C11-IN1-4 | Switch 10043 R FB
C11-IN1-5 | 
C11-IN1-6 | 
C11-IN1-7 | CBX BTN
C11-IN1-8 | Switch 10043 BTN
C11 Blocks | 
C11-B1-1 | Outside Inner B
C11-B1-2 | Outside Outer B
C11-B2-1 | CB Inner A
C11-B2-2 | CB Inner B
C11-B3-1 | CB Outer A
C11-B3-2 | CB Outer B
C11-B4-1 | SW141
C11-B4-2 | SW142

## Slide 14
Node C12 - West - Upper (cont'd)
C12-OU1 | 
C12-OU1-1 | Switch 10044 N
C12-OU1-2 | Switch 10044 R
C12-OU1-3 | Switch 10045 N
C12-OU1-4 | Switch 10045 R
C12-OU1-5 | Switch 10046 N
C12-OU1-6 | Switch 10046 R
C12-OU1-7 | Switch 10047 N
C12-OU1-8 | Switch 10047 R
C12-OU2 | 
C12-OU2-1 | S6-2 G
C12-OU2-2 | S6-2 Y
C12-OU2-3 | S6-2 R
C12-OU2-4 | S6-13 G
C12-OU2-5 | S6-13 R
C12-OU2-6 | S6-13 Y
C12-OU2-7 | S6-11 Y
C12-OU2-8 | C11 RELAY 1
C12-OU3 | 
C12-OU3-1 | S6-1 G
C12-OU3-2 | S6-1 Y
C12-OU3-3 | S6-1 R
C12-OU3-4 | S6-5 G
C12-OU3-5 | S6-5 Y
C12-OU3-6 | S6-5 R
C12-OU3-7 | S6-11 G
C12-OU3-8 | S6-11 R
C12-IN1 | 
C12-IN1-1 | Switch 10044 N FB
C12-IN1-2 | Switch 10044 R FB
C12-IN1-3 | Switch 10045 N FB
C12-IN1-4 | Switch 10045 R FB
C12-IN1-5 | Switch 10046 N FB
C12-IN1-6 | Switch 10046 R FB
C12-IN1-7 | Switch 10047 N FB
C12-IN1-8 | Switch 10047 R FB
C12-IN2 | 
C12-IN2-1 | Switch 10044 BTN
C12-IN2-2 | Switch 10045 BTN
C12-IN2-3 | Switch 10046 BTN
C12-IN2-4 | Switch 10047 BTN
C12-IN2-5 | 
C12-IN2-6 | 
C12-IN2-7 | 
C12-IN2-8 | 
C12 Blocks | 
C12-B1-1 | SW143
C12-B1-2 | SW144
C12-B2-1 | SW145
C12-B2-2 | SW146
C12-B3-1 | SW147
C12-B3-2 | PTT1
C12-B4-1 | PTT2
C12-B4-2 | TT

## Slide 15
Node C13 - Peninsula - Upper
C13-OU1 | 
C13-OU1-1 | Switch 10048 N
C13-OU1-2 | Switch 10048 R
C13-OU1-3 | Switch 10049 N
C13-OU1-4 | Switch 10049 R
C13-OU1-5 | Switch 10050 N
C13-OU1-6 | Switch 10050 R
C13-OU1-7 | S6-10 G
C13-OU1-8 | S6-10 R
C13-OU2 | 
C13-OU2-1 | S6-3 G
C13-OU2-2 | S6-3 Y
C13-OU2-3 | S6-3 R
C13-OU2-4 | S6-9 G
C13-OU2-5 | S6-9 Y
C13-OU2-6 | S6-9 R
C13-OU2-7 | S6-10 Y
C13-OU2-8 | C12 RELAY 1
C13-OU3 | 
C13-OU3-1 | S6-4 G
C13-OU3-2 | S6-4 Y
C13-OU3-3 | S6-4 R
C13-OU3-4 | S6-7 G
C13-OU3-5 | S6-7 Y
C13-OU3-6 | S6-7 R
C13-OU3-7 | 
C13-OU3-8 | 
C13-IN1 | 
C13-IN1-1 | Switch 10048 N FB
C13-IN1-2 | Switch 10048 R FB
C13-IN1-3 | Switch 10049 N FB
C13-IN1-4 | Switch 10049 R FB
C13-IN1-5 | Switch 10050 N FB
C13-IN1-6 | Switch 10050 R FB
C13-IN1-7 | 
C13-IN1-8 | 
C13-IN2 | 
C13-IN2-1 | Switch 10048 BTN
C13-IN2-2 | Switch 10049 BTN
C13-IN2-3 | Switch 10050 BTN
C13-IN2-4 | 
C13-IN2-5 | 
C13-IN2-6 | 
C13-IN2-7 | 
C13-IN2-8 | 
C13 Blocks | 
C13-B1-1 | SW148
C13-B1-2 | SW149
C13-B2-1 | SW150
C13-B2-2 | BW1
C13-B3-1 | BW2
C13-B3-2 | WH
C13-B4-1 | CB Siding
C13-B4-2 | CB Station